LOYOLA COLLEGE (AUTONOMOUS), CHENNAI – 600 034

B.Sc. DEGREE EXAMINATION – PHYSICS

FIFTH SEMESTER – NOVEMBER 2010

# PH 5404 / 5401 - ELECTRONICS - II

Date : 09-11-10 	Dept. No.	        Max. : 100 Marks

Time : 9:00 - 12:00

PART A

ANSWER ALL QUESTIONS                                            				10 x 2 = 20

- Draw the output waveform of an integrator for a square wave input.

- Draw the circuit diagram of a second order high pass filter.

- For a 5 bit R-2R ladder D/A converter, calculate the output for a digital input of 10101. Assume 0 = 0V and 1 = 5V.

- Differentiate between analog and digital signals.

- Give any four advantages of integrated circuits.

- Write a short note on linear IC’s.

- What is direct addressing mode? Explain with example.

- Write a short note on DAA instruction.

- What do pins ALE, HLDA denote in microprocessor 8085?

- What is the output of the following program?

MVI A, 03;	RLC;	RLC;	ADI, 01;	HLT

PART B

ANSWER ANY FOUR QUESTIONS                                            			4 x 7.5 = 30

- Solve the following differential equation using operational amplifiers.

d2y/dt2 + 2dy/dt + 3y – 1 = 0.

- With a neat diagram explain the working of a counter type A/D converter.

- Discuss in detail the classification of IC’s based on their structure.

- Write an assembly language program to determine the square root of a given number by indirect mode of addressing.

- Write a short note on arithmetic and logical instructions.

PART C

ANSWER ANY FOUR QUESTIONS                                            			4 x 12.5 = 50

- a. What is instrumentation amplifier? Explain it with a neat diagram 		(5)

b. Explain in detail an Op-Amp based monostable multivibrator with a neat diagram. 	   (7.5)

- a. Explain with circuit, the working of an op-amp based 4 bit binary weighted D/A converter.

b. For a 5 bit binary weighted resistor D/A converter network, determine the following 
(i) output voltage when LSB is set. (ii) Output voltage for 11010 (iii) Full scale voltage. Assume 0 = 0V and 1 = 10V. 			(6)

- Explain the fabrication of a bipolar transistor and explain how a bipolar transistor can be used as a diode.

- a. Write a short note on the different registers in microprocessor 8085.		(5).

b. Write an assembly language program to solve the given equation (x+y)/z by indirect mode of addressing.					(7.5).

- Write an assembly language program to sort the given set of 10 numbers in ascending order.

*******