LOYOLA COLLEGE (AUTONOMOUS), CHENNAI – 600 034

B.Sc. DEGREE EXAMINATION – PHYSICS

THIRD SEMESTER – NOVEMBER 2010

# PH 3504/PH 3502/PH 5501 - ELECTRONICS - I

Date : 30-10-10 	Dept. No.	        Max. : 100 Marks

Time : 9:00 - 12:00

PART  A

Answer  ALL  questions:     							     (10 x 2 = 20 marks)

- Define a Constant voltage source.

- State Maximum Power transfer theorem.

- What is Zero signal collector current? What is its significance?

- Define Class A Power amplifier. What is its maximum efficiency?

- Define CMRR of a differential amplifier. How can it act as a figure of merit of a difference amplifier?

- Define ‘Inversion Layer’ with reference to MOSFET.

- What input conditions of a JK flip flop makes it toggle?

- What is the difference between a Decoder & a Multiplexer?

- How many flip flops are required to store a decimal no.100110 in a binary register.

- Mention any two differences between ROM & RAM.

PART  B

Answer  ANY FOUR  questions:     					             (4 x 7.5  = 30 marks)

- A constant dc voltage of 10 volts is connected in series with resistances 4Ω & 3Ω. Another load resistance RL is connected across the 3Ω resistance. Use Norton’s theorem to determine the current through RL in the circuit.

- What is the need for biasing the transistor? Explain the Fixed Bias method and the disadvantages faced in this method of biasing.

- Draw the circuit of i) Summing & ii) Difference Amplifier using Op-Amp and obtain an expression for their output.

- Draw the logic circuit of a D- Flip Flop and explain its working. How it can be modified to function as a T flip flop?

- Explain with the circuit the working of a decade counter using JK – flip flops.

PART  C

Answer  ANY FOUR  questions:     		         			            (4 x 12.5 = 50 marks)

- Describe the analysis of a transistor amplifier in CE mode using ‘h’ parameter and obtain the expression for Ai, AV and Zi.

- Draw Phase Shift oscillator circuit using Transistor and explain its working.

- Explain the mechanism of current conduction in a SCR. Explain the action of SCR  as a half wave rectifier.

- Using K-map simplify the Boolean function:

F(A,B,C,D) = ∑(0,2,4,5,6,10,12,14). Implement the simplified expression using NAND gates only.

- Draw a 4-Bit RING counter using JK flip flops and describe the sequence of operations. What is the modulus of the counter?

$$$$$$$